Category:  Geberal Technology

Model numbers Tech note applies to:

All fiber

Brief Description:

Preventative Maintenance of Media Converters

Solution/Troubleshooting:

There is nothing specific that should be done as preventative maintenance to the device itself.  Most of the care should be taken when inserting the fiber optic cables or SFP modules.  However, the following guidelines for fiber optic cleaning and electrostatic discharge are listed below.

Fiber Optic Cleaning Guidelines

Fiber Optic transmitters and receivers are extremely susceptible to contamination by

particles of dirt or dust, which can obstruct the optic path and cause performance

degradation. Good system performance requires clean optics and connector ferrules.

1. Use fiber patch cords (or connectors, if you terminate your own fiber) only from

a reputable supplier; low-quality components can cause many hard-to-diagnose

problems in an installation.

2. Dust caps are installed at IMC Networks to ensure factory-clean optical devices.

These protective caps should not be removed until the moment of connecting

the fiber cable to the device. Should it be necessary to disconnect the fiber

device, reinstall the protective dust caps.

3. Store spare caps in a dust-free environment such as a sealed plastic bag or box

so that when reinstalled they do not introduce any contamination to the optics.

4. If it is suspected that the optics have been contaminated, alternate between

blasting with clean, dry, compressed air and flushing with methanol to remove

particles of dirt.

Electrostatic Discharge Precautions

Electrostatic discharge (ESD) can cause damage to any product, add-in modules or

stand alone units, containing electronic components. Always observe the following

precautions when installing or handling these kinds of products

1. Do not remove unit from its protective packaging until ready to install.

2. Wear an ESD wrist grounding strap before handling any module or component.

If the wrist strap is not available, maintain grounded contact with the system unit

throughout any procedure requiring ESD protection.

3. Hold the units by the edges; do not touch the electronic components or gold

connectors.

4. After removal, always place the boards on a grounded, static-free surface, ESD

pad or in a proper ESD bag. Do not slide the modules or stand alone units over

any surface.

Related Documents:

Accessories: