This document explains what value of gain we have to set in Labview.

The first, we can get the information of gain register from manual.

The corresponding setting value about Gain value is as below. (PCI-1710/1710L/1716/1716L)

So we have to transfer the binary value of B/U and Gain Code to decimal before we set it.

Example1:

If we want to use the input range”-10 to +10” and bipolar range, the binary value is 0 0 1 0 0(the second value is 0 because the register of this address is empty).

The transferred binary value to decimal is 4. So the gain value is 4.

Example2:

If we want to use the input range”0 to 2.5” and unipolar range, the binary value is 1 0 0 1 0(the second value is 0 because the register of this address is empty).

The transferred binary value to decimal is 16 + 2. So the gain value is 18.

It has the same rule to set the gain value in PCI-1711/1711L

But the S/D,B/U are not supported.

The corresponding setting value about Gain value is below. (PCI-1711/1711L)

The corresponding setting value about Gain value is below. (PCI-1710HG/1710HGL)

The corresponding setting value about Gain value is below. (PCI-1712/1712L/1732)